## Slide 1: Alpha wrapping with AN offset
Cédric Portaneri, Mael ROUXEL-LABBé, Michael Hemmer, David Cohen-Steiner, pierre Alliez
Notes: Todo:

## Slide 2: Motivation: Mesh validity
What is mesh validity?
A mesh is valid if it is:
2-manifold combinatorially and geometrically
Without self-intersections
Mesh validity is crucial to many applications in geometry processing and computer graphics
Moose [Jérémie Louvetz]
Boolean Operations
Segmentation
Remeshing & Simplification
Slicing
Computing distances
Simulations
Parameterization
Parameterization
Notes: Voice: Surface meshes are essential components in many geometry processing and computer graphics application. Most applications require, or at least prefer, input meshes that are combinatorially 2-manifold, watertight, and orientable.

## Slide 3: Motivation: mesh validity
Chevy Engine [GrabCAD]
Many meshes are not valid
Notes: Voice: Unfortunately, many mesh generation methods are imperfect and oftentimes produce meshes such as this engine mesh with many issues

## Slide 4: Motivation: mesh validity
Self-intersections
Non-manifoldness & spurious boundaries
Complex inner structures
Many meshes are not valid
Notes: Voice (cont.): Unfortunately, many mesh generation methods are imperfect and oftentimes produce meshes such as this engine mesh with many issues

## Slide 5: Problem statement
Input
3D model, possibly with defects
DESIRED Output
Watertight, manifold triangle mesh
No self-intersections
Enclosing the input
Unconditional robustness to input defects
Well-shaped (isotropic) triangles
Efficiency:
  Ignore inner structures
asdas
Notes: Voice: We address the problem of generating a watertight and orientable surface triangle mesh that strictly and tightly encloses the input. The algorithm must be robust to defects.

## Slide 6: Problem statement
Input
3D model, possibly with defects
DESIRED Output
Watertight, manifold triangle mesh
No self-intersections
Enclosing the input
Unconditional robustness to input defects
Well-shaped (isotropic) triangles
Efficiency:
  Ignore inner structures
  Controllable complexity of output
Notes: Voice (cont.): In particular, we wish to have a way to control the complexity of the output

## Slide 7: Approach
Bridging the gap between
Alpha carving
and
shrink wrapping
Notes: Voice: Our approach bridges the gap between a number of existing approaches by combining alpha shapes, mesh carving, and Delaunay-based meshing.

## Slide 8: Meshing
Algorithm overview
Start from a bounding box
Alternate two atomic operations:
  Carving: Get close to the input
  Delaunay refinement: Add freedom to enable getting close to the input
Maintain a valid boundary at all times
Notes: Voice: To create these points on the offset surface, we use an ambient 3D Delaunay triangulation and alternate carving and Delaunay refinement.

## Slide 9: CARVING
Notes: Voice: To create these points on the offset surface, we use an ambient 3D Delaunay triangulation and alternate carving and Delaunay refinement.

## Slide 10: REFINEMENT
Notes: Voice: To create these points on the offset surface, we use an ambient 3D Delaunay triangulation and alternate carving and Delaunay refinement.

## Slide 11: Algorithm illustration in 2D and 3D
Notes: Voice: Here is an illustration of the algorithm on a simple 2D model

## Slide 12: Algorithm illustration in 2D and 3D
Notes: Voice: Here is an illustration of the algorithm on a simple 2D model

## Slide 13: Results
Notes: Voice: We now present some applications to illustrate the usefulness of our method.

## Slide 14: Application to FLOW SIMULATION
small holes
panel gaps & overlaps
Bugatti model [Simscale], a defect-laden input
Multiple open connected components
Inner geometry
Degenerated elements
...
Notes: Voice: The following car model is riddled with all kinds of defect, making a flow simulation impossible. It also contains important inner geometry, which is irrelevant to the simulation.

## Slide 15: Application to flow simulation
Alpha Wrapping as input preprocessing for flow simulation
476k facets, 100s
[Simscale]​
Notes: Voice: Our method produces a closed, manifold mesh on which simulations can be run successfully.

## Slide 16: APplication to swepT volumes
242s
914s
Swept volumes by [RMAGS GmbH]
Input:
Very large mesh
Complex inner structures
All kinds of defects
Output:
Lower mesh complexity
Valid mesh with no internal elements
Faster sweeping
Conservative and tight w.r.t. to exact sweep
1.7M facets
57k facets
Notes: Voice: Our method can also be used as a preprocessing step before sweeping, drastically reducing runtime.

## Slide 17: Algorithm parameters
Guarantee closed 2-manifold mesh
Can also act as a defeaturing parameter, at the cost of tightness (similar to [Shewchuk 04])
Can be arbitrarily large or small
Controls the diameter of cavities to be explored
Acts as sizing field
Can be arbitrarily large or small
Alpha
Offset
alpha
offset
input
Notes: Voice: The behavior of the offset is similar to that of 𝛼 when it comes to features: small offset values ensure that the mesh is close to the input, and thus that it will capture well its geometry and features; on the other hand, large offset values act as a defeaturing tool.

## Slide 18: Strengths
Notes: Voice: We now expose the strengths of our method.

## Slide 19: OUTPUT Sensitive COMPLEXITY
Notes: Voice: The complexity of our algorithm depends primarily on the complexity of the output, meaning that complex inner structures have only a weak influence on the runtime, and no internal sampling is required.

## Slide 20: Robustness
Distance field-based approach: unconditional robustness to defects
Notes: Voice: Thanks to its formulation making only use of an implicit distance function and basic intersection predicates, our algorithm is immune to the usual defects found in many meshes.

## Slide 21: Correctness
Correctness: theoretical guarantees
Termination: using a 3D Delaunay triangulation enables use of the usual arguments (separation distance & packing argument)
No self-intersections, manifold: final surface mesh is extracted from a consistent underlying 3D triangulation
Closed, and enclosing the input: carving is disallowed if encroaching the input
Bounded one-sided Hausdorff distance (alpha + offset): faces of the output have a bounded Delaunay ball radius
Experimental Validation
Implementation: Code uses CGAL’s efficient exact predicates to ensure that theoretical guarantees are met.
Extensive assertions and tests: all checks are performed with exact computations, and the code is tested on large public datasets (Thingi10k, grabCAD, …)
https://www.cgal.org/
Notes: Voice: Basing our algorithm on extensively studied data structures such as the Delaunay triangulation enabled us to guarantee in theory a number of important properties: termination, validity, input enclosing, and distance bounds.

## Slide 22
THANK YOU
LAB DEMO TOMORROW
Thursday, August 11
11:10 am
West Building, Ballroom A/B
Notes: Voice: Thank you; code already available in CGAL. Join us at the SIGGRAPH Lab Demo in August for an extensive collaborative demo.